## Slide 1: 10 Methodological Overview
Leon Herrmann
Stefan Kollmannsberger
Chair of Data Engineering in Construction
Bauhaus-Universität Weimar
Deep Learning in Computational Mechanics – an introductory course, Herrmann et al. 2025
website
book
Notes: generated with https://www.the-qrcode-generator.com/

## Slide 2: Contents
9 Inverse Problems & Deep Learning
10.1 Simulation Substitution
  10.1.1 Data-Driven Modeling
  10.1.2 Physics-Informed Learning
10.2 Simulation Enhancement
  10.2.1 Pre-processing
  10.2.2 Physical Modeling
  10.2.3 Numerical Methods
  10.2.4 Post-Processing
10.3 Discretizations as Neural Networks
10.4 Generative Approaches
10.5 Deep Reinforcement Learning
11 The Future of Deep Learning in Computational Mechanics

## Slide 3: 10 Methodological Overview
Simulation substitution
  Data-driven modelling
  Physics-informed learning
Simulation enhancement
Discretizations as neural networks
Generative approaches
Deep reinforcement learning
Simulation with graph neural networks; DMD; Transfer learning
Hamiltonian/Lagrangian neural networks; SINDy; (PINNs)
Input-convex neural networks for material modeling; EUCLID; Neural networks as ansatz function of inverse quantities; Superresolution; Differentiable physics
Hardware acceleration with GPUs; (HiDeNN)
Generative design; Realistic data generation; Anomaly detection; Transformers for natural language processing
Control engineering tasks: autonomous flight; robots;
Alternative gradient-free optimizer
Deep learning in computational mechanics: a review, Herrmann et al. 2024

## Slide 4: 10.1.1 Data-Driven Modeling
The aim of data-driven modeling is to learn a model in a supervised manner relying on labeled data
Neural network as approximation of function relating the data
The quality of prediction is defined in terms of a data misfit function, e.g., the MSE
Covered in depth in Chapter 3

## Slide 5: 10.1.1 Data-Driven Modeling
Consider the PDE
Goal is the approximation of a forward operator
Or an inverse operator
For simplicity, we limit ourselves to the forward operator
With a dataset , the forward operator is learned
The quality of prediction is defined in terms of a data misfit function, e.g., the MSE
Covered in depth in Chapter 3

## Slide 6: 10.1.1 Data-Driven Modeling
10.1.1.1 Space-Time Approaches
Time can simply be treated in the same way, as any other spatial dimensions
In the following, time is no longer mentioned explicitly, but included in the coordinates
10.1.1.2 Time-Stepping Procedures
Time is treated in a discrete manner using relying on a time-stepping procedure

## Slide 7: 10.1.1 Data-Driven Modeling
Fully-Connected Neural Networks
Image-to-Image Mapping
where and are evaluations of and
  on a uniform grid for convolutional neural networks
  on arbitrary grids for graph neural networks
Model Order Reduction Encoding
Forward operator is learned on a reduced space with inverse mapping
Dimensional reduction can be performed with principal components analysis, singular value decomposition, autoencoders
Misfit to data can be formulated on reduced space or full space
Covered in depth in Chapters 3 & 6

## Slide 8: 10.1.1.1.4 Neural Operators
DeepONet
Operator prediction is split up into two tasks
  Prediction of basis functions
  Prediction of coefficients
  Prediction of solution at with coefficients with the scalar product

## Slide 9: 10.1.1.1.4 Neural Operators
Fourier Neural Operators
Mapping of coefficients to solution is learned on a uniform grid
Fourier Neural Operator (FNO) consists of Fourier Layers that operator in Fourier Space (over )

## Slide 10: 10.1.1.1.4 Neural Operators
Fourier Neural Operators
Expressive and efficient architecture
  Enhance the non-local expressivity
  Fast Fourier transforms enable computational efficiency

## Slide 11: 10.1.1.2 Time-Stepping Procedures
Time-Stepping Procedures
Problem is discretized in time with
Prediction of time-history with fully-connected neural network
Prediction of time-history with recurrent neural network
  or variations, such as LSTM, GRU, transformers
Difference to fully-connected neural network is a hidden/latent state that propagates infromation from prior steps

## Slide 12: 10.1.1.2 Time-Stepping Procedures
Dynamic Mode Decomposition
Consider two successive snapshot matrices
Goal is to identify linear operator that captures the dynamics
Solved as a regression using the Moore-Penrose pseudoinverse
Dynamical predictions with linear operator
Only valid for linear dynamics
Koopman operator theory states, that it is possible to represent any nonlinear system as a linear one by using an infinite-dimensional Koopman operator that acts on a transformed state
In practice, finite dimensional approximation, i.e., also for
Constructed with a dictionary of orthonormal basis functions

## Slide 13: 10.1.1.2 Time-Stepping Procedures
Dynamic Mode Decomposition with neural networks
Learn dictionary with a neural network
  Training on mismatch between predicted state and the true state in the dictionary space
  Reconstruction using Koopman mode decomposition
Learn augmented state with autoencoder (learns both encoding and decoding)
  Loss can be formulated in terms of autoencoder reconstruction, linear dynamics, future state prediction
is obtained with conventional DMD

## Slide 14: 10.1.2 Physics-Informed Learning
Incorporation of physical constraints
via penalty terms, which acts as regularization
  For example physics-informed neural networks as seen in Chapters 4 & 5
by construction, which reduces the learnable space
  For example physics augmented neural networks for material modeling as seen in Chapter 7

## Slide 15: 10.1.2 Physics-Informed Learning
Again, we consider Space-Time Approaches first
In general, we consider a PDE with boundary & initial conditions
And focus on the forward operator
To illustrate the upcoming methods, consider the differential equation of a static elastic bar
with Dirichlet boundary conditions on
and/or Neumann boundary conditions on

## Slide 16: 10.1.1.2.1 Differential Equation Solving
Physics-Informed Neural Networks
Solution to one differential equation is approximated with neural network
Cost function is expressed as residual of the differential equation
residual of boundary conditions (and initial conditions)
and a data-driven cost
Covered in depth in Chapter 4

## Slide 17: 10.1.1.2.1 Differential Equation Solving
Deep Least-Squares Method/Deep Galerkin Method
Considers the norm of the residual over the entire domain (instead of individual collocation points)
Variational Physics-Informed Neural Networks
Residual of the weak form instead of the residual of the strong form
Test functions are chosen by the user, e.g., trigonometric or polynomial
Weak Adversarial Networks
Test functions are modeled with a second neural network
Minimax optimization (competition between trial and test functions)
Covered in depth in Chapter 5

## Slide 18: 10.1.1.2.1 Differential Equation Solving
Deep Energy Method/Deep Ritz Method
Minimization of the potential energy
Only applicable to conservative systems, i.e., systems that conserve energy
Not generally applicable to inverse problems
  going towards in and towards on minimizes to an arbitrary level
Covered in depth in Chapter 5

## Slide 19: 10.1.1.2.1 Differential Equation Solving
Extensions: Boundary Conditions
Enforcement of boundary conditions with penalty term, leads to unbalanced optimization:
Strong enforcement of boundary conditions: a priori satisfaction
  is a smooth interpolation of boundary conditions
  is a signed distance function (zero at boundary)
For Neumann boundary conditions, prediction of and derivative with separate neural networks
For complex domains: learn in a supervised manner
Weighting terms for each loss term
  Treated as hyperparameters, or learned with minimax optimization
The residual at each collocation point is treated as an equality constraint (augmented Lagrangian)

## Slide 20: 10.1.1.2.1 Differential Equation Solving
Extensions: Ansatz
Use convolutional neural networks instead of fully connected neural networks
  Irregular geometries: binary encodings, signed distance functions, coordinate transformations
    Numerical differentiation instead of automatic differentiation necessary
    Or interpolation with, e.g., splines
Use graph neural networks instead of fully connected neural networks
Classical basis, such as FE or IGA: Approximate coefficients with neural network
  Construct discretization in the classical sense and use discretized residual as loss
  Forward problem: learn , inverse problem: learn
  Also interpreted as mapping a neural network to a finite element space (or interpolation)
    When coefficients are predicted using coordinates
Parametrization of ansatz with to learn multiple solutions

## Slide 21: 10.1.1.2.1 Differential Equation Solving
Extensions: Domain Decomposition
Split complex problem in multiple simple problems
hp-vPINNs decompose domain into patches
  Piece-wise polynomial test functions on each patch & global solution : separation of integration
Conservative PINNs utilize one neural network per patch
  Interface constraints enforce the conversation laws across patches, e.g., flux
  Allows parallelization and adaptivity (shallow network for smooth, deep network for complex solutions)
Generalization for any PDE presented as extended PINNs
  Interface constraint formulated in terms of difference in solution and difference in residual

## Slide 22: 10.1.1.2.1 Differential Equation Solving
Extensions: Acceleration Methods
Transfer learning from base task
Improved sampling strategies
  Importance sampling (collocation density proportional to residual)
  Adaptivity: collocation points are added if residual is large
Derivative of loss should be zero at minimum: include in loss
Improved formulations of the loss: quality of solution does not necessarily correspond to loss
  One improvement relies on the norm
Numerical differentiation instead of automatic differentiation
Extreme machine learning: all layers except the last one are frozen. The last layer is linear and learned through a least-squares regression
Adaptive activation functions
Spiking neural networks
Specialized hardware to improve efficiency of training neural networks
In particular for higher order derivatives, as seen in Chapter 5

## Slide 23: 10.1.2.1.2 Inverse Problems
Discovery of Governing Equations
AI-Feynman is an automated framework for symbolic regression
Performs dimensional analysis, polynomial regression and brute force search algorithms sequentially
If an interpretable equation is not recovered
  Neural networks as interpolation of the data
  Test for symmetry, e.g., if then introduce variable
  Test for separability, i.e., , to split equation in simpler parts

## Slide 24: 10.1.2.2 Time-Stepping Procedures
Time-Stepping Procedures
For simplicity, we assume a differential equation of the form
For systems, we assume the following form
Parareal PINNs
Temporal domain is split in subdomains.
Simplified PDE is solved from timestep . PINN corrects solution in all subdomains
Simplified PDE is solved from timestep PINN corrects solution in all subdomains
…

## Slide 25: 10.1.2.2 Time-Stepping Procedures
PINN: Discrete Time Model
Relies on the Runge-Kutta method with stages
where , which is to be approximated with a neural network
Loss is computed by rearranging the Runge-Kutta equations using the initial condition

## Slide 26: 10.1.2.2.2 Inverse Problems
Discovery of Governing Equations
Learn right hand-side with neural network
  Minimization of residual of differential equation (PINN)
  Use with any time-stepping scheme
Interpolation of observed with neural network in a supervised manner
  Assume a linear network for right hand side with inputs for right hand side
  regularization to enforce sparsity
  Due to linearity, the model is interpretable

## Slide 27: 10.1.2.2.2 Inverse Problems
Discovery of Governing Equations
PDE-Net: Learns right hand side with specialized convolutional neural network
Each convolution is designed to represent one spatial derivative term
Achieved with special constraints, such that the neural network is only able to adjust order of approximation
Forward Euler method
Comparison to measurements
Both coefficients to derivative terms and order of approximation of derivatives are learned
Identification of system and equation-specific approximations of the derivatives

## Slide 28: 10.1.2.2.2 Inverse Problems
Discovery of Governing Equations
Sparse Identification of Nonlinear Dynamic Systems (SINDy)
Snapshot matrices of state and its time derivative
Formulation as sparse regression problem solved with sequential thresholded least squares/LASSO
Expressivity can be increased by coordinate transformations enabling simpler dynamics
  Similar to DMD, an autoencoder can be used to learn both encoding and decoding
  Both autoencoder parameters and are learned by gradient descent
    regularization to enforce sparsity
    Limited interpretability
  Classical time-stepping scheme can be applied in reduced space
Covered in depth in Chapter 6

## Slide 29: 10.1.2.2.2 Inverse Problems
Discovery of Governing Equations
Consider multistep methods (similar to the PINN discrete time model)
With defining the scheme
Right-hand side is approximated by a neural network
Loss is expressed in terms of multistep scheme

## Slide 30: 10.2 Simulation Enhancement
Simulation Chain
Pre-Processing
Physical Modeling
Numerical Methods
Post-Processing
General Procedure
Replace a function in the simulation chain by a neural network
The remaining simulation chain remains unchanged

## Slide 31: 10.2.1 Pre-processing
Pre-Processing
Geometry extraction
  Segmentation, e.g., visual crack detection in images
Mesh generation
  Prediction of mesh density
Data preparation
  Denoising of measurement data
  Low-frequency extrapolation in seismic data
Preconditioning
  Prediction of initial solution for classical solver
  Transfer learning for neural networks

## Slide 32: 10.2.1 Physical Modeling
Physical Modeling
Model Substitution
  Neural network as surrogate (not interpretable)
  Incorporation in simulation
Identification of Model Parameters
  Under assumption of model structure, neural network identifies the model
  Neural network is not incorporated in simulation
Model Identification
  Neural network discovers model
  Neural network is not incorporated in simulation
Consider the example of consitutitve models: Identify the stress-strain relation
  Directly usable in a finite element framework
Covered in depth for material modeling in Chapter 7

## Slide 33: 10.2.1 Physical Modeling
Model Substitution
Neural network as replacement of stress-strain relation trained in a supervised manner
No guarantee, that physical principles are upheld, such as the second law of thermodynamics, material objectivity/frame invariance, material symmetry/isotropy, polyconvexity
Specialized network architectures to guarantee physical principles by construction
  Prediction of strain energy from invariants
  Input-convex neural networks or neural ordinary differential equations for poly-convexity
Training in a supervised manner with stress-strain data
Training in an unsupervised manner via incorporation in finite element solver in combination with measurements of simulation using, e.g., modified constitutive relation error

## Slide 34: 10.2.1 Physical Modeling
Identification of Model Parameters
Assumption of material model, e.g., linear elasticity
  Prediction of model parameters from spatially varying Young‘s modulus
Can for example be used for homogenization

## Slide 35: 10.2.1 Physical Modeling
Model Identification
Efficient unsupervised constitutive law identification and discovery (EUCLID)
  Posed as regression problem (inspired by SINDy)
  Strain energy density expressed in terms of candidate functions with invariants
  Stresses are obtained by deriving
  Residual is formulated in weak form of the momentum balance and solved with fixed-point iteration
  Extension with neural networks, where is learned by ensemble of neural networks instead of candidate functions (interpretability is lost)

## Slide 36: 10.2.1 Physical Modeling
Model Identification
Automated discovery through interpretable neural networks
Strain energy density of example

## Slide 37: 10.2.3 Numerical Methods
Numerical Methods
Numerical Quadrature, find optimal positions and weights
  Particle Swarm optimization to find optimal , : train neural network in a supervised manner
Correction of strain-displacement matrix for distorted elements
Learn optimal test functions
Learn optimal timestep based on time-history

## Slide 38: 10.2.3 Numerical Methods
Numerical Methods
Multiscale methods
  Element substructuring
    Network predicts displacements and stresses from boundary conditions in meta-element
    Equilibrium is computed through assembly and iterative solution procedure
  Zooming methods
    Network predicts global system response
    Boundary conditions are extracted and used for local analysis
Active Learning
  Neural network is trained during employement
  Neural network is always used and an error estimator asseses the quality of the prediction
  If prediction is bad, classical method computes solution
  Every bad predictions, the neural network is retrained

## Slide 39: 10.2.3 Numerical Methods
Numerical Methods
Optimization
  Gradient-based optimization
    Prediction of state from parameters with forward operator
    Quality of prediction determined by cost function
    Gradient of cost function is used to update parameters
Covered in depth in Chapter 9

## Slide 40: 10.2.3 Numerical Methods
Numerical Methods
Injecting deep learning in the optimization
  Replacement of forward operator with surrogate model
    Faster forward prediction
    Simplified and possibly faster gradient computation
  Replacement of sensitivity computation with surrogate model
    Learned in a supervised manner
    Learn indirectly by maximizing the improvement of the cost function
      Possibility for active learning
    Partial replacement by solving coarse sensitivity problem and refinement with neural networks
  Direct prediction of update from current state (skip the entire loop by going from to )
    Prediction of final state or intermediate states
  Neural network as ansatz of
    Neural network acts as regularizer/discovery of better local optima

## Slide 41: 10.2.4 Post-Processing
Post-Processing
Modification of results to ensure manufacturability
Feature extraction
  Subsequent shape optimization
Solution enhancement: Coarse to fine to reduce numerical errors
  Solve problem on coarse and fine grid, train neural network in a supervised manner
    Forward problems
    Inverse problems, e.g., increasing resolution of identified designs
    Sensitivity computation, i.e., solving adjoint problem on coarse grid

## Slide 42: 10.2.4 Post-Processing
Coarse to fine: tight integration with the solver
PDE is solved on coarse grid
Right-hand side is approximated by NNs using gradients as input
Gradients are expressed as
where are predicted by neural network (with constraints)
Right-hand side is used with time-stepping scheme to predict from
Loss is defined in terms of coarsened fine scale solution
Training on fine scale solutions on small domains
Equation specific discretization of gradients to enable stable time-stepping procedures on coarse grids

## Slide 43: 10.2.4 Post-Processing
Coarse to fine
PDE is to be solved on coarse grid
At each timestep coarse solution is corrected by corrector network
Network is corrected using coarsened fine solution
Important detail: during training corrector network is applied after each timestep in the solver.
  Adjoint state method to obtain gradients through the solver
  This way, the network is trained the way it later will be employed
  Outperforms purely supervised approach
  Methodology is called differentiable physics

## Slide 44: 10.3 Discretizations as Neural Networks
Finite Element Method
Finite element neural networks
  Consider the system of equations from a finite element discretization
  Assuming constant material properties along an element and uniform elements: pre-integration
  Inserting assembly into system of equations

## Slide 45: 10.3 Discretizations as Neural Networks
System of equations
Comparison to structure of a FNN
Two layer FNN without activation and bias
Prediction of forces to establish a loss
In forward setting is learnable
In inverse setting is learnable

## Slide 46: 10.3 Discretizations as Neural Networks
Finite Element Method
Hierarchical deep-learning neural networks (HiDeNNs)
Shape functions are treated as neural networks constructed from basic building blocks
Consider one-dimensional linear shape functions
Elemental displacement from nodal displacements treated as shared neural network weights
nodal positions and nodal displacements are learnable weights
One-dimensional finite elements
One-dimensional finite elements as NN
Covered in depth in Chapter 5
Moving nodal positions during solving is equivalent to r-refinement in the finite element method

## Slide 47: 10.3 Discretizations as Neural Networks
Finite Difference Method
Finite difference stencils can be considered as convolutional kernels
Consider 1D scalar wave equation
With a finite difference discretization
Can be written in terms of convolutional kernels
Iterative application through time results in a recurrent neural network
Inverse problem can be posed with these RNNs by solving forward problem and learning input parameters, e.g., or
This is not truly a recurrent neural network due to the lack of a hidden state

## Slide 48: 10.3 Discretizations as Neural Networks
The discretized wave equation as analog recurrent neural networks
Input encoded as signal
Output measured and integrated at probing locations
For example for classification of sounds
Trainable region could be 3D-printed as an analog neural network for classification

## Slide 49: 10.3 Discretizations as Neural Networks
Material Discretizations
Deep material networks construct neural networks from material distributions
  Basic building blocks from analytical homogenization techniques
  Output material tensor is obtained by two input material tensors , which are homogenized and rotated
  Learnable parameters are the volume fractions and the rotations
  Application: from stress-strain data from multiple microstructure samples
    Extraction of material properties of te phases, anisotropic characteristics, or volume fractions

## Slide 50: 10.3 Discretizations as Neural Networks
Neural Differential Equations
Evaluation of one recurrent unit in a recurrent neural network
Can be viewed as an Euler discretization of the following ODE
Instead of using the recurrent evaluations of an RNN, the ODE is considered as a network
  Input is the initial condition
  Output is the solution at time
  Gradients are obtained through the adjoint state method in an ODE solver
Extension to partial differential equations, where convolutional neural networks act as spatial gradients

## Slide 51: 10.4 Generative Approaches
Variational autoencoder
Generative adversarial network
Flow-based model
Diffusion model
Transformer
Covered in depth in Chapter 8

## Slide 52: 10.4 Generative Approaches
Applications
Data Generation
  Microstructures (specialized architectures relying on RNNs/transformers to go from 2D to 3D)
  Designs
Optimization
  Parametrization of design space with subsequent shape optimization
  Variational autoencoder GANs are popular, due to well-behaving gradients
  Incorporating vague constraints
    Design diversity by increasing novelty/creativity
    Similarity to old designs, due to aethetics or manufacturability
      Pixel-wise distance to previous designs
      Style transfer loss
  Inverse problems
    Generator predicts material distribution
    Discriminator says, if it is correct based on a forward simulation
Covered in depth in Chapter 8

## Slide 53: Generative Approaches
Applications
Conditional Generation
  Rendered cars from sketches
  Hierarchical shape generation (child shape considers ist parent shape)
  Topology optimization from initial fields defined by boundary conditions
  Generation from physical properties
    Design with specific compliance
    Material distribution resulting in a specific seismogram
  Super-resolution GANs for coarse simulation data (tempoGAN)
  cycleGANs for invertible functions without need for paired data
Anomaly Detection
  Generative approach learns a distribution of structures
    If the generative method is unable to reconstruct a structure, it must be an anomaly
    In the case of GAN, a larger discriminator loss indicates an anomaly
    In the case of an autoencoder, the latent space may also be considered
Covered in depth in Chapter 8

## Slide 54: 10.5 Deep Reinforcement Learning
Learning from interaction with environment
  Agent performs actions
  Based on actions, environment returns state and reward
Deep reinforcement learning uses a neural network for the agent
Value-based methods
  Estimates value function
  Take action that maximizes value function
Policy-based methods
  Maps states to actions directly
Actor-critic methods
  Combine value-based and policy-based methods
  Actor chooses policy
  Critic evaluates chosen action (the actor adjusts action according to the evaluations of the critic)

## Slide 55: Contents
9 Inverse Problems & Deep Learning
10.1 Simulation Substitution
  10.1.1 Data-Driven Modeling
  10.1.2 Physics-Informed Learning
10.2 Simulation Enhancement
  10.2.1 Pre-processing
  10.2.2 Physical Modeling
  10.2.3 Numerical Methods
  10.2.4 Post-Processing
10.3 Discretizations as Neural Networks
10.4 Generative Approaches
10.5 Deep Reinforcement Learning
11 The Future of Deep Learning in Computational Mechanics

## Slide 56: 10 Methodological Overview
Leon Herrmann
Stefan Kollmannsberger
Chair of Data Engineering in Construction
Bauhaus-Universität Weimar
Deep Learning in Computational Mechanics – an introductory course, Herrmann et al. 2025
website
book
Notes: generated with https://www.the-qrcode-generator.com/