## Slide 1: 6 Machine Learning in Computational Mechanics
Leon Herrmann
Stefan Kollmannsberger
Chair of Data Engineering in Construction
Bauhaus-Universität Weimar
Deep Learning in Computational Mechanics – an introductory course, Herrmann et al. 2025
website
book
Notes: generated with https://www.the-qrcode-generator.com/

## Slide 2: Contents
5 Advanced Physics-Informed Neural Networks
6.1.1 Singular Value Decomposition
6.2 Reduced Order Models
6.3 Sparse Identification of Non-Linear Dynamical Systems – SINDy
6.4 Clustering
6.5 Support Vector Machines
7 Material Modeling with Neural Networks

## Slide 3: 6.1.1 Singular Value Decomposition
Singular value decomposition is a unique matrix factoriziation ()
With
Matrices are obtained through eigendecompositions of and
Columns of consist of the eigenvectors of
Columns of consist of the eigenvectors of
Diagonal entries of are the square roots of the corresponding eigenvalues
Signs of the eigenvectors of and must be consistent and can be checked with
If an entry of is negative, the signs of the corresponding eigenvector in or must be flipped.
is the conjugate transpose of
Non-zero eigenvalues of and are the same
are unitary matrices, i.e., (for real matrices: orthogonal matrices)

## Slide 4: 6.1.1 Singular Value Decomposition
Singular value decomposition as dimensionality reduction technique
Economy singular value decomposition
Exact reconstruction of with truncated (for )
Truncated singular value decomposition: truncation of beyond the mismatch in dimensionality

## Slide 5: 6.1.1 Singular Value Decomposition
Truncated singular value decomposition: truncation of beyond the mismatch in dimensionality
are truncated up to singular value
Reconstruction is now approximative!
The truncated singular value decomposition enables dimensionality reduction
  Principal components analysis is a related dimensionality reduction technique (see 6.1.2)

## Slide 6: 6.1.1.1 Image Compression
Image compression as example of dimensionality reduction with singular value decomposition
Gray-scale image as matrix with pixel entries in and direction
Truncated singular value decomposition leads to values instead of values
Singular values (diagonal entries of )
Original image ()

## Slide 7: 6.1.1.1 Image Compression
Compression ratios for :
Further compression possible if multiple images are considered simultaneously, i.e., a common compression, e.g., eigenfaces from a library of faces can reconstruct yet unseen faces
Low-dimensional procedure for the characterization of human faces, Sirovich et al. 1987

## Slide 8: Exercises
E.22 Singular Value Decomposition (P & C)
  First, perform a singular value decomposition on a given matrix. Next implement a general singular value decomposition and apply it to an image.

## Slide 9: 6.1.1.2 Identification of a Reduced Basis
Consider the spatio-temporal function
Measurements obtained at temporal snapshots on a spatial grid with points
(stored in a snapshot matrix )
Singular value decomposition of snapshot matrix
Spatial modes can be extracted from columns of
Temporal modes can be extracted from columns of
Only the first 3 modeshapes are associated with non-zero singular values:
can be reconstructed exactly with

## Slide 10: 6.1.1.2 Identification of a Reduced Basis
Modeshapes identified from using singular value decomposition
provide a reduced basis (using time-dependent coefficients )
Consider a system of equations (task is to solve for )
Prior knowledge of the solution is stored in the snapshot matrix
Singular value decomposition yields , i.e.,
Projection into a lower dimensional system
Solve for instead of and recover with
Exploiting the orthonormal property of ()

## Slide 11: Exercises
E.23 Introduction to Reduced Order Models (C)
  Sample a basic spatio-temporal function and extract the essential spatial and temporal modes using a singular value decomposition

## Slide 12: 6.2 Reduced Order Models
Acceleration of a dynamic finite element simulation using a reduced basis
Consider the semi-discrete finite element equations
Solvable by integration through time, e.g., central difference approximation of
Inserted in the finite element equations
Rewritten in an explicit form
Compute next time step by inverting
is the mass matrix, is the stiffness matrix, is the source vector

## Slide 13: 6.2.2 Reduced Order Modeling with Finite Elements
From a snapshot matrix
A reduced basis is identified (with the truncated singular value decomposition)
Projection of degrees of freedom onto reduced basis
Insertion into the semi-discrete finite element equations
Pre-multiplication with to project the system onto the reduced space (to reduce number of equations to )
Solve for and recover full solution vector with
Proper orthogonal decomposition: projection of solution (to differential equation) to lower-dimensional subspace using orthogonal basis functions
degrees of freedom with equations

## Slide 14: 6.2.3 Cantilever Beam
Simulation of a cantilever beam with two-dimensional finite elements
Full finite element simulation for timesteps with degrees of freedom
Singular value decomposition on to obtain reduced basis
  Identification of the first four mode shapes of an Euler-Bernoulli beam

## Slide 15: 6.2.3 Cantilever Beam
From the singular values, a truncation level of is selected (reducing the system from to )
Measurement for snapshot matrix
Simulation with reduced order model
Full system: s per time step
Reduced system: s per time step

## Slide 16: Exercises
E.24 Reduced Order Models with Finite Elements (C)
  Modify a finite element code to incorporate a reduced order model. After collecting a snapshot matrix and performing a singular value decomposition, the reduced basis is to be applied within the system of equations.

## Slide 17: 6.3 SINDy
SINDy: Sparse Identification of Non-Linear Dynamical Systems
The goal of SINDy is the discovery of sparse dynamical system models described by systems of differential equations of the form
Where
Discovering governing equations from data: Sparse identification of nonlinear dynamical systems, Brunton et al. 2015

## Slide 18: 6.3 SINDy
1. Sample temporal snapshots of and its first temporal derivative in snapshot matrices
2. Select a library of candidate functions for the sparse regression
3. The sparse regression problem with sparse regression coefficients
4. Compute the sparse regression coefficients with
Sequential thresholded least squares
(or Lasso)
If the temporal derivatives are unavailable, numerical schemes can be used
Least squares with a penalty to promote sparsity

## Slide 19: 6.3 SINDy – Sequential Thresholded Least Squares
The regression is solved iteratively with least squares. In each iteration the coefficients smaller than a threshold are set to zero. This results in a sparse coefficient matrix

## Slide 20: 6.3.1 Learning a Differential Equation
A system of differential equations is given as
With the initial conditions
And with the solution
The goal of SINDy is to find the underlying differential equation with snapshots of the solution

## Slide 21: 6.3.1 Learning a Differential Equation
Snapshots collected at
Selected candidate functions and the corresponding matrix

## Slide 22: 6.3.1 Learning a Differential Equation
Sparse regression problem solved with sequential thresholded least squares with
Initial least squares regression

## Slide 23: 6.3.1 Learning a Differential Equation
Recovered system
Original system

## Slide 24: 6.3.2 Structural Dynamics Model
A two degree of freedom mass-spring-damper model
Governing equations obtained from equilibrium
And initial conditions

## Slide 25: 6.3.2 Structural Dynamics Model
Governing equations obtained from equilibrium
Substitutiono to transform the system of second order differential equations into a system of first order differential equations
Any higher order system of differential equations can be rewritten in terms of a system of first order differential equations

## Slide 26: 6.3.2 Structural Dynamics Model – Linear
Assuming linear springs and dampers
Example values SINDy estimation with 300 snapshots and the original system
Measurement
Prediction with SINDy

## Slide 27: 6.3.2 Structural Dynamics Model – Linear
SINDy is made for nonlinear dynamics
Nonlinear springs and dampers
SINDy estimation with 500 snapshots and the original system
Measurement
Prediction with SINDy

## Slide 28: Exercises
E.25 Introduction to SINDy (P & C)
  Apply SINDy to a simple system of first order differential equations using pen-and-paper. Next implement SINDy and the sequential thresholded least sqaures algorithm and recompute the pen-and-paper computations.
E.26 SINDy for Structural Dynamics (P & C)
  Apply the implementation of SINDy to a two-degree-of-freedom example from structural dynamics.

## Slide 29: 6.4 Clustering
Clustering: Discovers similarities between data and creates discrete clusters (unsupervised)
One approach is -means clustering
Subdivision of dataset into clusters
Each datapoint belongs to cluster with the closest mean
Framed as minimization problem
Where is the mean of the cluster consisting of datapoints associated with the cluster, i.e.,
NP-hard problem, solved by heuristic algorithms, e.g., Lloyds algorithm
Computation of distances , used to identify closes cluster by taking the minimum distance
Recomputation of cluster centers with the mean of the associated data points
Repeat until convergence

## Slide 30: 6.4 Clustering – Lloyds algorithm

## Slide 31: 6.4.1 Cross-Section Clustering
Consider the cross-section of an I-beam with the properties
Assuming three different cross-sections (with different distributions)
Can we identify the three different cross-sections from the three properties, ?

## Slide 32: 6.4.1 Cross-Section Clustering
-means clustering with Lloyds algorithm
Original cross-sections
Identified cross-sections with clustering
slice
slice
slice
Cluster centers are indicated by silver centers

## Slide 33: 6.4.1 Cross-Section Clustering
Evolution of cluster identification in -slice (initial guess + three iterations
Iteration 0:
Iteration 1:
Iteration 2:
Iteration 3:

## Slide 34: 6.5 Support Vector Machines
Classification: Prediction of a discrete category via a mapping between input and a (discrete) category
Support vector machines as classification algorithm
Binary classifier, i.e., (-1 and 1)
Predecessor of neural networks
Linear support vector machines construct a hyperplane between two categories
Hyperplane should maximize margin between closest points to the hyperplane
Minimal margin
Maximal margin

## Slide 35: 6.5 Support Vector Machines
Prediction is made depending on what side of the plane the datapoint lies
Optimization is formulated
1. Correct classification of data
  With the constraint
2. Maximization of the margin
Loss is not differentiable and therefore exchanged with the differentiable Hinge loss function
Optimization via gradient-based optimization determines optimal hyperplane
Ensures that closest data points (support vectors) are at a standardized distance
Mislabeling a datapoint increases the loss by one
Achieved by the regularization term

## Slide 36: 6.5 Support Vector Machines – Examples
Linear support vector machine applied to the cross-section example
Nonlinear support vector machine enabled by projection to higher-dimensional space

## Slide 37: Contents
5 Advanced Physics-Informed Neural Networks
6.1.1 Singular Value Decomposition
6.2 Reduced Order Models
6.3 Sparse Identification of Non-Linear Dynamical Systems – SINDy
6.4 Clustering
6.5 Support Vector Machines
7 Material Modeling with Neural Networks

## Slide 38: 6 Machine Learning in Computational Mechanics
Leon Herrmann
Stefan Kollmannsberger
Chair of Data Engineering in Construction
Bauhaus-Universität Weimar
Deep Learning in Computational Mechanics – an introductory course, Herrmann et al. 2025
website
book
Notes: generated with https://www.the-qrcode-generator.com/